## Slide 1
CASE STUDY · ENGINEERING ETHICS
The Boeing 737 MAX
How a hidden flight-control system, certification shortcuts, and a culture of cost pressure led to 346 deaths.
Trinity College · Engineering Lab · Final Ethics Presentation

## Slide 2
ROADMAP
Where we're headed
01
Background
The MAX program & competitive pressure
02
MCAS Explained
What the system did and why it existed
03
The Two Crashes
Lion Air 610 & Ethiopian Airlines 302
04
Root Causes
Engineering, sensor, and process failures
05
Ethical Analysis
Where decision-making broke down
06
Lab Connections
What our coursework tells us about this
Boeing 737 MAX | Engineering Ethics Case Study
2

## Slide 3
BACKGROUND
A new engine, an old airframe
Boeing's 1960s-era 737 was the company's bestseller. When Airbus launched the fuel-efficient A320neo in 2010, Boeing needed a fast, cheap response.
Rather than design a new aircraft, Boeing fitted the 737 with much larger, more efficient LEAP-1B engines. To fit them under the low 737 wing, the engines had to be moved forward and up.
This changed how the airplane handled — it had a tendency to pitch up at high angles of attack. MCAS was created in software to mask that tendency, so pilots wouldn't need new simulator training.
THE PRESSURES
MARKET
Beat the Airbus A320neo to market
COST
Avoid full simulator retraining for airlines
SPEED
Re-certify quickly under existing 737 type rating
Boeing 737 MAX | Engineering Ethics Case Study
3

## Slide 4
THE SYSTEM
What MCAS actually did
Maneuvering Characteristics Augmentation System
Trigger: high angle-of-attack (AOA) reading
Action: automatically pushes nose down via horizontal stabilizer
Input: a single AOA sensor (no redundancy used)
Disclosed to pilots? No — omitted from manuals & training
FAILURE CHAIN
1
Faulty AOA sensor
Single sensor reports false high-angle data
2
MCAS activates
System believes plane is stalling
3
Stabilizer trims down
Nose pushed toward ground
4
Pilots fight back
MCAS re-engages every ~10 seconds
Boeing 737 MAX | Engineering Ethics Case Study
4

## Slide 5
THE TRAGEDIES
Two crashes, five months apart
LION AIR 610
October 29, 2018
189
lives lost
ROUTE
Jakarta → Pangkal Pinang
FLIGHT TIME
11 minutes after takeoff
Crashed into the Java Sea. Investigators traced the cause to a faulty AOA sensor and repeated MCAS activations the pilots could not diagnose.
ETHIOPIAN 302
March 10, 2019
157
lives lost
ROUTE
Addis Ababa → Nairobi
FLIGHT TIME
6 minutes after takeoff
Crashed in a field 39 mi from departure. Crew followed Boeing's post-Lion Air checklist but could not recover; the MAX fleet was grounded worldwide within days.
Boeing 737 MAX | Engineering Ethics Case Study
5

## Slide 6
ROOT CAUSES
What went wrong
Single-Point Sensor Design
MCAS relied on input from one AOA sensor — no cross-check. A single faulty reading was enough to trigger a fatal command.
Compromised Certification
Boeing employees acted as FAA-designated reviewers. The 'delegation of delegation' meant Boeing helped decide what the FAA would scrutinize.
Hidden from Pilots
MCAS was deliberately omitted from training manuals to avoid triggering simulator-training requirements that would have cost airlines money.
Cost & Schedule Pressure
Internal communications showed engineers were pushed to keep changes minimal — even when test data flagged MCAS as potentially catastrophic.
Boeing 737 MAX | Engineering Ethics Case Study
6

## Slide 7
ETHICAL ANALYSIS
Where ethics broke down
Engineering codes of ethics (NSPE, IEEE, ASME) share a clear hierarchy: public safety comes first, ahead of employer interests or competitive position.
PRINCIPLES VIOLATED
Public safety first
Cost and schedule were prioritized over disclosure of a flight-critical system.
Honesty & transparency
MCAS was hidden from pilots; the FAA was not informed of a late-stage authority increase.
Whistleblower duty
Internal concerns from engineers and test pilots reportedly did not flow up the chain.
WHAT THE CODE DEMANDS
Treat safety-critical software as such
Single-sensor inputs and silent authority over flight controls require full safety review.
Disclose, don't disguise
If a system can override pilots, pilots must be trained on it — period.
Independent oversight
Regulators must verify, not delegate, the assessment of catastrophic-class hazards.
Boeing 737 MAX | Engineering Ethics Case Study
7

## Slide 8
LAB TIE-IN
How this connects to our lab work
Every failure on this slide is a problem we've practiced solving in lab — but at engineering scale, with lives in the balance.
LAB TOPIC
WHAT IT MEANS FOR THE 737 MAX
Data collection & sensor input
MCAS read a single AOA sensor with no cross-check — the engineering equivalent of using one thermocouple and trusting the number.
Errors & uncertainty in measurement
Sensors fail. Our labs propagate uncertainty; safety-critical aerospace systems must do the same and design for sensor disagreement.
System characterization
The MAX's pitch-up tendency was a known characteristic 'fixed' in software. Characterizing the underlying physical behavior is non-negotiable.
Presenting & communicating data
Engineers documented MCAS risks internally — but the information never reached pilots or regulators. Communication is part of the engineering work.
Boeing 737 MAX | Engineering Ethics Case Study
8

## Slide 9
CONSEQUENCES
Aftermath & assessment
346
lives lost
20 mo.
global fleet grounding
$2.5B+
DOJ settlements & fines
OUR ASSESSMENT
Boeing's decisions were not the result of a single bad actor. They were the predictable output of a system that rewarded speed over safety, treated software as a place to hide hardware compromises, and let the regulated party shape the regulator's scope.
In 2024 Boeing agreed to plead guilty to conspiracy to defraud the FAA — but the deeper lesson for engineers is that ethics is not a final-stage compliance check. It's a load-bearing element of every design decision we make.
Boeing 737 MAX | Engineering Ethics Case Study
9

## Slide 10
KEY TAKEAWAYS
Engineering ethics is engineering.
Safety-critical systems demand sensor redundancy and fail-safe behavior — always.
If a design choice depends on hiding information from end users, that's the warning sign.
Cost, schedule, and competition are real — but they live below public safety in the priority stack.
Engineers have a duty to escalate; organizations have a duty to listen.
Questions?